## Slide 1: CRANE 4 BOOMS MODEL_E 3D LAG CSYS
UNITS : m:kg:s:Pa:N:K
Boom
Extension
Fixed
Boom
Rotation
Fixed
Hook
Load
(400N)
Gravity Load
(Weight)
Initial Crane Angle = 40.7637
Actuator
P Controlled
(NON WRAPPER SCENARIO)

## Slide 2
SCENARIOS BOOM VARIABLE INITIAL PID FUNCTIONAL
ROTATION EXTENSION CONFIGURATION LOAD CONTROLLER MOCKUP(FMU)
MODEL_A YES YES HORIZONTAL GRAVITY NO NO
MODEL_B NO NO ANGLE + GRAVITY + NO NO
EXTENSION HOOK
MODEL_C NO NO ANGLE + GRAVITY + YES NON WRAPPER
EXTENSION HOOK (PROPORTIONAL)
MODEL_D NO NO ANGLE + GRAVITY + YES WRAPPER
EXTENSION HOOK (PROPORTIONAL)
MODEL_E NO NO ANGLE + GRAVITY + YES NON WRAPPER
EXTENSION HOOK (PROPORTIONAL)
NB
Model_E scenario the internal and external cylinders/pistons are not functional.
Model _E scenario has gravity and hook load applied and the data is valid up to 1.5s.
The booms are in a fixed configuration (ie angle and extension).
A vertical actuator is positioned at the connection point between the external piston and boom section 1.
This actuator has a P Controller and holds the crane at the given initial angle(40.7706deg) of the crane boom.
Non Wrapper scenario. Force by actuator holds up the crane booms.

## Slide 3
SET POINT
P CONTROLLER POINT
ACTUATOR
NB The Y direction difference between NID 25082 and NID 5589 is to be kept to a minimum via the P Controller

## Slide 4
NON-WRAPPERS
WRAPPERS
NB. WRAPPER SCENARIO
PRIMARY
(MASTER)
SECONDARY
(SLAVE)
COSIMULATION TERMINOLGY

## Slide 5
FOLDER STRUCTURE
etc
etc

## Slide 6
etc
LS_DYNA FILES FOR COSIMULATION
Initial Crane Angle = 40.7637

## Slide 7
SOFTWARE INSTALLATION
Pyfmi version 2.9.5
Anaconda version 2020.11

## Slide 8
HOW TO INSTALL

## Slide 10
GEOMETRY
(AVERAGE)
BOOM WIDTH HEIGHT THICKNESS LENGTH STIFFENERS WIDTH HEIGHT
  0.358 0.358 0.005 3.745 1 0.005 0.005
  0.338 0.338 0.005 2.025 2 0.005 0.005
  0.318 0.318 0.005 1.950 3 0.005 0.0045
  0.299 0.299 0.005 1.876

## Slide 11
INTERNAL & EXTERNAL PISTON/CYLINDER PARTS
(Not All Parts in Crane Model used in the Calculations)
NB Initial Configuration
Initial Crane Angle = 40.7637

## Slide 12
Initial Crane Angle = 40.7637

## Slide 13
SCENARIO E

## Slide 14
TYPICAL PARTS
ELASTIC/PLASTIC
RIGID

## Slide 15
KEYWORDS CONTROL
KEYWORDS BOUNDARY CONDITION
KEYWORDS CONSTRAINTS
NSID 1400
NSID 1500
Actuator

## Slide 16
KEYWORDS BOUNDARY PRESCRIBED MOTION
Initial Crane Angle = 40.7637
NB Both Internal & External Piston not Functional

## Slide 17
KEYWORDS CONTACT 1
CONTACT 112
CONTACT 123
CONTACT 134
Boom 2
Boom 4
Boom 3
Boom 1 Stiffeners
Boom 2 Stiffeners
Boom 3 Stiffeners

## Slide 18
KEYWORDS CONTACT 3
CONTACT 2530
CONTACT 4550
CONTACT 6570
Initial Crane Angle = 40.7637

## Slide 19
KEYWORD GRAVITY & HOOK LOADS
Hook
Load
Gravity Load
LOADING CURVE
Initial Crane Angle = 40.7637

## Slide 20
RESULTS NODE TRACE
Initial Crane Angle = 40.7637
Angle Vibration About Initial Crane Angle
Fixed
Fixed
Actuator Holds Up the Crane Booms

## Slide 21
BOOM ROTATION & EXTENSIONS
Boom
Extension
Boom
Rotation
NB Crane Booms Fixed in Rotation and Extension
Hook Load
Initial Crane Angle = 40.7637
Actuator Controls Boom Angle

## Slide 22
BOUNDARY CONSTRAINT FORCES
X, Y & Z FORCES
TOTAL FORCE
FILTERED BW 60Hz
FILTERED BW 60Hz
Initial Crane Angle = 40.7637

## Slide 23
CONTACTS
Boom 4
Boom 3
Boom 2
Boom 1 Stiffeners
Boom 3 Stiffeners
Boom 2 Stiffeners
FILTERED BW 60Hz
Initial Crane Angle = 40.7637
These Contacts are between a Boom Section and a Boom Stiffener

## Slide 24
CONTACTS
Boom 4 Lock
Boom 3 Lock
Boom 2 Lock
Boom 1 Stiffeners Max Limit
Boom 3 Stiffeners Max Limit
Boom 2 Stiffeners Max Limit
NB These Contacts prevent The Boom Sections from Retracting
Initial Crane Angle = 40.7637
FILTERED BW 60Hz

## Slide 25
VON MISES STRESS

## Slide 26
Actuator Force (P Controlled) vs Time
ACTUATOR Y DIRECTION FORCE
P Controller Gain = 2000000
Set Point
P Controller Point
Actuator

## Slide 27
MODEL_E
NON WRAPPER SCENARIO
LS_DYNA is PRIMARY(MASTER)
No Third Party Software is involved
All calculations are done within LS_DYNA
LS_DYNA interacts through the FMU, Folder fmu_tpl, File fmi.udf.c
Actuator Force calculated automatically.